## Slide 1: Air Quality Index Mapping Using Model, Regulatory Monitor, and Sensor Data in Real-Time
Scott A. Epstein, Ph.D.
Program Supervisor, Air Quality Assessment
Planning, Rule Development and Area Sources

## Slide 2: Acknowledgements
South Coast AQMD Air Quality Assessment Group
Melissa Sheffer, Senior Meteorologist; Mark Bassett, PhD; Melissa Maestas, PhD; Xiang Li, PhD; Elham Baranizadeh, PhD; Nico Schulte, PhD
Notes: I would first like to start by acknowledging all of the members of the AQ Assessment group that helped do a lot of the work shown in this presentation.

## Slide 3: The South Coast AQMD
17 million residents
4 counties
3 air basins:
  South Coast
  Salton Sea (Riverside County portion)
  Mojave Desert (Riverside County portion)
Non-attainment of federal PM2.5, ozone, and PM10
Typically over 150 exceedance days per year

## Slide 4: Current Methods of Displaying Real-Time Air Quality Data
South Coast AQMD “Proxy Method”
AirNow Inverse Distance Weighted Interpolation
www.aqmd.gov/aqdata
www.airnow.gov
Limitations identified:
Location of monitor that is driving an area’s current AQI is unclear
Distance-weighted interpolation doesn’t account for complex terrain
Public often looks at multiple maps to understand current air quality (PurpleAir map) and does not interpret low-cost sensor data appropriately
Some regions in the “Proxy” map are too large to accurately represent localized events
Notes: Unclear to residents where the monitors are that are measuring the pollutants that drive the current AQI

## Slide 5: Monitor/Model/Sensor Blended Map
5
Schulte, N., Li, X., Ghosh, J.K., Fine, P.M., Epstein, S.A. Responsive High-Resolution Air Quality Index Mapping Using Model, Regulatory Monitor, and Sensor Data in Real-Time, accepted in Environmental Research Letters
Pollutant | Method | Far from monitors | Near monitors
PM2.5 | Fill in gaps between monitors using forecasts* and low-cost sensor data | Models and low-cost sensor data drive concentration | Monitor data drives concentration
O3 | Fill in gaps between monitors using forecasts* | Models drive concentration | 
PM10, NO2, CO | Natural neighbor interpolation | Monitor data drives concentration | 

## Slide 6: The User Experience

## Slide 7: The User Experience
Pollutant | AQI
PM2.5 | 70 (calculated)
O3 (8 hr) | 207 (measured)
PM10 | 60 (measured)
NO2 | 8 (measured)
CO | 3 (measured)
San Bernardino
AQI: 207
AQI Category: Very Unhealthy
Dominant Pollutant: Ozone 8 Hr Average

## Slide 8: Treatment of Low-Cost Sensor PM2.5 Data
Quality Control PurpleAir Data
  By comparing the simultaneous measurements from the two channels within each sensor and applying statistical criteria
Calibrate PurpleAir Data
  Using collocated BAM data and correction for relative humidity
Combine individual sensors to estimate the average concentration in a grid cell
  To “smooth” variation from local source impacts, we average at least 3 sensors in each grid cell

## Slide 9: Can We Trust the Low-Cost Sensor Data?
Not calibrated
Calibrated
645,000 hourly data points (Purple Air with collocated FEM) are used to derive a calibration equation
Calibration equations adapted from: Malings et al, 2019. Aerosol Science & Technology

## Slide 10: Blending Monitor/Model/Sensor Data
Chart: Spatial Position
| -1 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
Monitor | 10 | 16 | 21 | 15
Chart: Spatial Position
| -1 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
Monitor | 10 | 16 | 21 | 15
Sensor | 35 | 10
y3 | 10 | 16 | 25 | 21 | 15
Monitor/Model
Smoothed Monitor/Model/Sensor
Concentration “surface” is fixed to regulatory monitors. Between monitors, model and low-cost sensor data modifies the concentration surface based on their relative uncertainties.

## Slide 11: Evaluating Performance Compared to Other Methods
x
x
Monitor
…
Error 1
Error 2
Error n
x
…
Leave one out cross validation used for all pollutants
Root Mean Square Error (all pollutants)
IDW – Inverse distance weighting as used by AirNow maps
Pollutant | Proxy | IDW | Blended
PM2.5 [μg m-3] | 7.6 | 7.73 | 5.94
O3 [ppb] | 10.2 | 8.75 | 7.12
PM10 [μg m-3] | 34.7 | 36.1 | 33.6
CO [ppm] | 0.171 | 0.191 | 0.163
NO2 [ppb] | 7.57 | 6.94 | 6.22
Blended map has lower errors than Proxy and IDW approach for all pollutants used in AQI calculation

## Slide 12: Additional Evaluation of PM2.5 Performance with Monitoring Data from Independent Data Sets
PM2.5 Root Mean Square Error []
Method | Proxy | IDW | Blended
Gravimetric | 4.64 | 4.07 | 3.59
North Hollywood | 8.91 | 9.07 | 7.51
Mission Viejo | 8.83 | 7.31 | 8.87
24-hour Average Gravimetric Data (June 30, 2018 – March 31, 2020)
  Performed analysis at 11 sites that do not have collocated continuous PM2.5 monitors
North Hollywood Hourly PM2.5 (Oct 11, 2019 – March 31, 2020)
Mission Viejo Hourly PM2.5 (Oct 29, 2019 – March 31, 2020)
Gravimetric, North Hollywood, and Mission Viejo monitor data are not used by interpolation or by NOAA model

## Slide 13: Additional Advantages of Blended Map During Wildfires
Blended map automatically integrates e-BAM monitoring data
Integration of PurpleAir and NOAA model data helps capture localized smoke plumes that are between regulatory monitors
Higher resolution blended map better represents wildfire plumes

## Slide 14: Map Performance Excels During Wildfires
PM2.5 RMSE [] on fire days
Method | Proxy | IDW | Blended
Leave One Out Cross Validation | 7.04 | 6.62 | 6.01
Gravimetric validation dataset | 5.68 | 4.39 | 3.35
North Hollywood validation dataset | 19.2 | 16.8 | 9.15

## Slide 15: Our Progress
Presentations of Blended Map
NACAA’s fall membership meeting in October 2019
CAPCOA planning symposium in October 2019
EPA Air Quality Analysis Group in March 2020
CARB Monitoring team in March 2020
CARB AQMIS team in May 2020
Imperial County APCD in June 2020
EPA Center for Environmental Measurement and Modeling in July 2020
PurpleAir in August 2020
Deployment Schedule
Paper accepted to Environmental Research Letters in July 2020
Operational version of scripts running for several months. Scripts will be finalized by Early September.
Website version and mobile app version currently under development and expected in next few months

## Slide 16: Conclusions
Advantages of the Blended Map:
  More accurate than previous methods, especially during wildfires
  More transparent as it clearly distinguishes calculated and measured concentrations
  Helps the public interpret low-cost sensor data and its inherent uncertainties
  Provides a higher spatial resolution than South Coast AQMD proxy map

## Slide 17: Backup Slides

## Slide 18: Process to Generate AQI Values
Compute AQI for each pollutant
Compute Maximum AQI (of all pollutants)
Interpolate all pollutants for the current hour
Compute 8 hour ozone and 24 hour PM2.5 and PM10 using nowcast

## Slide 19: PurpleAir Calibration
Not calibrated
Calibrated
RMSE = 4.6

## Slide 20: PurpleAir Calibration
Not calibrated
Calibrated

## Slide 21: Sensor Blending Method
Quality control, calibrate, and smooth (average in grid cell) the PurpleAir data
Residual Kriging interpolation with modifications
  PurpleAir data is included as observations in addition to monitor data
  Data is assigned a measurement uncertainty that is used to give more weight to the more accurate monitor data
Measurement Uncertainty
  PurpleAir uncertainty is the sum of two components: the RMSE of the collocation curve fit1 and the standard error of the average in the grid cell2
  Monitor data has zero uncertainty
  1 As 1 standard deviation
  2 Standard error is estimated based on the average concentration when the number of sensors is small

## Slide 22: Using Gravimetric Monitor Data to Evaluate Performance
24-hour PM2.5 average of blended map predictions are compared to gravimetric measurements at stations without collocated continuous instruments
Performance is somewhat station dependent
Blended map has lower average RMSE than Proxy and IDW

## Slide 23: Including PM10 Measurements from Surrounding Areas Produces More Realistic AQI